## Slide 1: A Servo Controller for Brushed DC Motor
Presented by:
Bashir Tawfig Bashir Abugharsa (1181102921)
Supervisor:
Dr. Lo Yew Chiong
Moderator:
Dr. Cham Chin Leei

## Slide 2: TABLE OF CONTENT
Background Overview
Scopes and Objectives
Problem Statement
Literature Review
Methodology
Result and Discussion
Timeline
Summary
Acknowledgement
References

## Slide 3
Background Overview
Brushed DC motors are integral in mechanical systems evolution due to their simple structure and cost-effectiveness.
They are favored for their DC power source. These motors are popular in mass-produced products.
However, advanced applications require precision that exceeds basic controller’s capabilities.
Servo Controller Solution Offers refined motor control via feedback mechanisms for precise operation.

## Slide 4
Problem Statement
Precision Limitation: The basic mechanical design of Brushed DC motors hinders precise control using just standard driver circuits.
Control Challenges: Traditional circuits cannot fine-tune speed and position accurately, failing in applications needing exact motion.
Performance Variables: External factors like load changes affect motor performance, which is unaddressed by simple drivers.
Advanced Needs: High-precision tasks demand more than what basic control circuits provide, requiring a more advanced approach to motor control.

## Slide 5
Project Scope
Goal: Develop a servo controller to improve the precision of Brushed DC motors in speed and positioning.
Driver Circuit Design: Create a PWM-controlled circuit using a microcontroller for speed control.
PID Control System: Implement a PID closed-loop control integrated with the driver circuit for more precise control.
Dynamic Performance: Ensure that the motor consistently follows precise movement while automatically adjusting for variations in load.
Outcome: To achieve a higher standard of motor precision suitable for advanced, modern applications, enabling efficient and accurate operation under various conditions.

## Slide 6
Objectives
User-Interactive Control: Implement a serial communication protocol for immediate, precise control adjustments.
Accurate Speed & Position Management: Develop a closed-loop system utilizing optical encoder feedback for precise motor handling.
Real-Time PID Control: Engineer a PID system for stable and accurate motor response.
Adaptive System Calibration: Establish a tuning methodology for optimal performance under diverse conditions and uses.

## Slide 7: Literature Review
Motor Driver Circuit Design
Ayyanathan and Mariyammal[1] explore the use of Pulse Width Modulation (PWM) for controlling DC motor speed, employing an AT89S52 microcontroller and L293D IC. This method excels in providing precise control over small DC motors in a cost-effective manner. However, the reliance on L293D IC limits its applicability to small motors, posing a challenge for more complex operational contexts.
Figure 1: Bi-directional Rotation Using a Full-Bridge

## Slide 8: Literature Review
Motor Driver Circuit Design
Figure 2:H- Bridge Motor Driver Circuit
V. Gupta [2] designed H-bridge motor driver circuit for wheeled mobile robots. The use of BJTs in this design provides a cost-effective solution, but it falls short in terms of efficiency and power management compared to MOSFETs, which could affect its performance in more demanding robotic applications.

## Slide 9: Literature Review
PID Controller Design
Figure 4: H- Bridge Motor Driver Circuit
X. Zhang [3] used fuzzy logic with PID control to enhance the system’s adaptability and robustness. However, the use of fuzzy logic adds computational complexity.
Z. Adel, A. A. Hamou, and S. Abdellatif implemented a real-time PID control system on an Arduino Mega 2560, complemented by MATLAB for interface and real-time monitoring. However, their reliance on a speed sensor may limit the system's precision for applications demanding high accuracy.
Figure 3: A Closed-loop PMDC Motor Speed Control Scheme Based on PID Controller

## Slide 10
Methodology
Brushed DC Motor Driver Circuit
Microcontroller Firmware
Main Components
Tools

## Slide 11
Methodology
Brushed DC Motor Driver Circuit
H-Bridge Configuration: Utilizes four power MOSFETs to form the brushed DC motor driver circuit.
Motor Control: H-Bridge circuit controls motor direction and speed via a PWM signal.
PWM Generation: A microcontroller is used for generating the PWM signal required for motor control.
Gate Driver IC: Manages the operation of MOSFETs.

## Slide 12
Methodology
Brushed DC Motor Driver Circuit

## Slide 13
Methodology
Microcontroller Firmware

## Slide 14
Methodology
Main Components
IRF3205 N-channel MOSFET
IR2110 MOSFET Gate Driver:
VOFFSET: 500V max.
IO+/- 2A / 2A.
VOUT 10 - 20V.
ton/off (typ.) 120 & 94 ns.

## Slide 15
Methodology
Main Components
STM32f103 Microcontroller
LM7805 & LM7812 Voltage Regulator

## Slide 16
Methodology
Hardware Tools
Hantek Oscilloscope / Multimeter
Adjustable Power Supply
ST-Link Programmer
USB to TTL Adapter

## Slide 17
Methodology
Software Tools
STM32CubeIDE
Arduino IDE Serial Monitor
Autodesk Fusion 360

## Slide 18: Future Implementation (FYP 2)
Develop a real-time PID control system.
1
Precisely adjust the PID controller for optimal speed and position accuracy.
Design a PCB for the motor driver circuit.
Use Optical Encoder as feedback loop.
3
4
2

## Slide 19
Result and Discussion
First slide be a photo of the circuit.
-CW speed 40% 90%. One at motor, low and high side gate, controller, show serial monitor
-CCW speed 40% 90%. One at motor, low and high side gate, controller, show serial monitor
-check diode effectiveness
-power consumption for mosfets, regulators and ICs???

## Slide 20
Project Timeline

## Slide 21: Project Budget

## Slide 22
Summary

## Slide 23
References
[1] Ayyanathan, Mariyammal. "DC Motor Speed Control Using PWM." 2018, vol. 3, pp. 2456-2165. [Online]. Available: https://www.researchgate.net/publication/338116979_DC_Motor_Speed_Control_Using_PWM
[2] V. Gupta, "Working and analysis of the H - bridge motor driver circuit designed for wheeled mobile robots," 2010 2nd International Conference on Advanced Computer Control, Shenyang, China, 2010, pp. 441-444, [Online]. Available: https://ieeexplore.ieee.org/document/5486818
[3] X. Zhang, "Design and implementation of fuzzy PID DC motor control system based on STM32," in 2023 IEEE International Conference on Control, Electronics and Computer Technology (ICCECT), Jilin, China, 2023, pp. 1129-1131, [Online]. Available: https://ieeexplore.ieee.org/document/10141000
[4] Z. Adel, A. A. Hamou and S. Abdellatif, "Design of Real-time PID tracking controller using Arduino Mega 2560for a permanent magnet DC motor under real disturbances," 2018 International Conference on Electrical Sciences and Technologies in Maghreb (CISTEM), Algiers, Algeria, 2018, pp. 1-5, [Online]. Available: https://ieeexplore.ieee.org/document/8613560

## Slide 24: Thank You